## Slide 1: 天马望远镜单天线终端及数据处理
吴亚军，上海天文台
虚拟天文台与天文信息学2019年会
大庆，2019/11/27-30

## Slide 2: Contents
The Tianma Radio Telescope
The Backends
  DIBAS: for Spectroscopy and Pulsar;
  Spectrometer: for Spectroscopy
  FRB: Real-time detecting;
The Data
  Observation and Data
  Database

## Slide 3: The Tianma telescope
Ka2
K7

## Slide 4: The Backends and Sciences
终端：数据采集、处理和存储；
技术与科学的桥梁

## Slide 5: The Backends
DIBAS
Spectrometer
Real-time FRB

## Slide 6: DIBAS
Imported from NRAO；
Support for Spectroscopic and Pulsar Observations
3 Bank, each 1.5GHz Bandwidth;

## Slide 7: The Spectrometer: Background
DIBAS(now)：3 Banks, each 1.5 GHz BW;
Background:
  Sensitivity is good;
  Ka/Q Band: > 10GHz BW, line survey;
  7-element K Receiver in design;
  Need more banks, high resolution
3-hours observation on IRC10216, velocity range(-12000~12000 km/s), 1
HC7N(14-13)
HC5N(6-5)
HC9N(29-28)
HC7N(15-14)

## Slide 8: The spectrometer: Hardware
5Gsps ADC, Xilinx Kintex7 FPGA; 10Gb网络；
Version 1
Version 2
Improve the interface between ADC and FPGA

## Slide 9: The spectrometer: Synthesizer and ADC
Synthesizer:
Fin(MHz) |  | 20190927 | 20190927 | 20190929
 | ENOB | ENOB | ENOB | ENOB
10 | 7.33 | 7.31 | 7.30 | 7.29
110 | 7.19 | 7.25 | 7.23 | 7.23
210 | 6.87 | 7.25 | 7.34 | 7.27
410 | 6.17 | 6.79 | 6.78 | 6.76
810 | 5.43 | 6.94 | 6.86 | 6.81
1210 | 4.93 | 6.60 | 6.46 | 6.36
1610 | 4.51 | 5.96 | 6.27 | 6.24
1810 |  |  | 5.89 | 6.04
ADC ENOB
1
2
3
The performance of Spectrometer

## Slide 10: The spectrometer: FPGA Code
Mode1 in progress; others in plan;
FPGA, Software, and Control in discussion;
Mode | Window(s) | Bandwidth （MHz） | Channel(s) | Freq. Resolution(KHz) | Velcity Resolution(Km/s) @10GHz | processor
Mode1 | 1 | 2048 | 131072 | 15.625 | 0.468 | FPGA
Mode2 | 2 | 256 | 65536 | 3.906 | 0.117 | FPGA
Mode3 | 8 | 32 | 65536 | 0.488 | 0.015 | FPGA+GPU
Mode1
10 MHz in
noise in

## Slide 11: The real-time FRB detection: Background
Instrument:
  CHIME/ASKAP are powerful (400-800 MHz);
  Other bands are necessary;
  Real-time detection is convenient when other observations
FRB：
  Short Bright radio pulses;
  High Dispersion Measure(DM)
  Observe:
    Origin;
    Frequency range
    Repeating
    Polarization
    …
FRB121102, GBT, 4-8 GHz
Detection rate at Tianma
From Luo Rui, PKU

## Slide 12: The real-time FRB detection: Hardware
Dual Channel 1Gsps ADC, 8-bit;
Xilinx K7480t FPGA
10Gb Ethernet for data
H-maser for frequency standard
ADC+FPGA+GPU for Digital backend
GPU Storage Server
Intel® Xeon® Processor E5 2.2GHz 28 core;
128G DDR Ram
GeForce GT 1030 GPU
40 TB storage
1U Rack

## Slide 13: The real-time FRB detection: Pipeline
FPGA
CPU/GPU
Real-time pipeline:
PFB: 1024 Channels
Clean RFI: clean frequency range
De-dispersion: dedisp with GPU
Detect: Candidate as SNR > 6, then Recording

## Slide 14: The real-time FRB detection: pulsar
Early in 2018, test the Pipeline
Giant Pulse of B0531+21
Record the data, then pipeline
S band, clean at 2180-2280 MHz

## Slide 15: The real-time FRB detection: RRAT
RRAT (rotating radio transient) J1819-1458
Signal detected
Real-time
Further analysis

## Slide 16: The real-time FRB detection: FRB
Repeating FRB121102, 20 hours(S, C band), NO Detection;
Strange RFI, the fake candidate;

## Slide 17: The Backends: Conclusion
Wide-band, Universal, Transient detection, raw data recording;
Multi-feed; Array
逐步扩展至多功能终端

## Slide 18: The Data
  Observation and Data
  Database

## Slide 19: Observation
自动化的观测设置、数据预处理、用户数据拷贝；
用户通过FTP下载和查看观测数据；

## Slide 20: Data
The Doppler to be included in future

## Slide 21: Database
正在建立谱线数据库；
212373数据文件，校准后的频谱；
初步完成了根据字段关键词进行检索
继续完善功能；
后续扩展至脉冲星

## Slide 22: Database: future plan
数据检索
分类下载
在线数据处理及存储
数据可视化
硬件与软件的配置

## Slide 23: Thanks for Attentions!